## Slide 1: Server Administration Tools
Lecture 10

## Slide 2: Server Administration Tools
UPS (pp.607-611)
Scheduler (pp. 625-630)
Directory Replication (pp. 630-636)

## Slide 3: UPS or Whats wrong with my power?
Spikes: are massive voltage impulses that last for a split second, they are often caused by lightning, static, or large machinery
Surges: are higher voltages that last for more than one second. Smaller increase than spikes. Surges often happen when large electrical machinery is switched off.
Sags: are the opposite of surges. The voltage dips suddenly for a moment, usually because large equipment was switched on.

## Slide 4: Even more power bugs
Noise: high frequency signals that travel along the power supply lines. Noise is caused by radio transmission, lightning and computer power supplies.
Brownouts: are long-term lower than normal voltages, lasting for minutes or even hours. This usually happens when the power supply in your area is overtaxed. (e.g. when transformers are down)

## Slide 5: And more...
Ground loops: are power impulses between linked devices.
Electromagnetic interference is generated by radio transmitters, fluorescent lights, even computer accessories.

## Slide 6: UPS
Uninterruptible power supply (UPS): A device that provides immediate battery power to equipment during a power failure or brownout for a limited time period
Online UPS: Battery backup device that provides power to equipment directly from its batteries at all times
Offline UPS: Battery backup device that waits until there is a power decrease or sag before switching to battery power

## Slide 7: kVA versus Watts
Volt-Amps, or VA, is the amount of apparent power supplied to equipment, or volts x amps.
Wattage is the actual amount of the power that is available to do work, and is always less than or equal to the VA rating.
The ratio of watts to VA is the "power factor" of the equipment
An Ammeter is the most reliable method to gauge actual use.

## Slide 8: Offline UPS
Passes through incoming mains power to the output sockets while the supply is good.
It monitors the line constantly for a major voltage drop that signifies power failure.
It then switches on it's inverter (converts DC to AC) and supplies output power
There is power loss during switchover, but typically of around five milliseconds, which is insignificant to most loads.

## Slide 9: Online UPS
All the incoming power is always converted to direct current, which both tops up the batteries and feeds the inverter.
The inverter is a constant-duty inverter, so this costs a little more.
There is also a fail-safe mechanism known as a Static Bypass which on detecting failure in the inverter will throw the load on the mercy of the mains supply, rather than letting it drop altogether..

## Slide 10: Online vs. Offline
UPSs above 5kVA in size are almost universally on-line in design.
It is difficult to produce an on-line economically below around 600VA, so most UPSs below this size are off-line.

## Slide 11: UPS Control Panel Applet (UPS.CPL)

## Slide 12: Scheduler
Similar to cron utility on Unix
Scheduler service must be activated in Services applet before first use
Can run jobs as system user or any other designated user
Can run in the background even when nobody is logged on at the console
Enter jobs with the AT command or via the Command Scheduler.

## Slide 13: Scheduling jobs with the AT command (p. 628)
Most commonly used syntax: AT [\\computer] time /INTERACTIVE /EVERY:
Specify day-of-week or day-of-month
Examples: AT \\barney 00:05 /every:su c:\jobs\weekly.bat AT 09:00 /next:Tuesday c:\jobs\report.bat AT 2 /D
Avoid using /INTERACTIVE unless you have no choice

## Slide 14: Directory Replication
Most common use: copying logon scripts and policy files from PDC to BDCs
Can be used on any data shared between computers or domains
It is a dynamic service that continuously identifies changed and new files and copies them.
It will remove files or create subdirectories as necessary to keep them identical

## Slide 15: Import and Export Servers
Export Server must be NT Server
Import Server can be NT Server or Workstation
An NT Server can be both an export and import server at the same time

## Slide 16: Configuring an export server
You must designate the following items:
Export directory: all subdirectories and files beneath the directory can be exported
Export To list: list of computers and domains which will import the files
When exporting to a domain, every computer configured to import the files will receive them
One computer can only export one replication tree.

## Slide 17: Using the Directory Replicator service
Create an account that is a member of the Replicator local group
Every import and export server must be running Directory Replicator service
Trust relationships must be set up as usual
Use Server Manager to configure exports and imports.