## Slide 1: CNT211
Lecture 2
1/20

## Slide 2: Agenda
Campus safety and security
Author Eric S. Raymond on campus
Win2000 update
Revisit CNT 211 website
Review lecture #1
CH.3 Your Job as Administrator
CH.4 Planning and Installing Network Media
Lab shakedown exercise

## Slide 3: Campus safety and security
Escort Services - Staff, Students and guests may request a security escort from any location on campus to any other location on campus by contacting the Office of Campus Safety and Security at extension #3411.
Motorist Assists - Security staff will provide vehicle jump-start assistance. leave their lights on, etc. The Office of Campus Safety and Security will help you call for a tow truck. http://www.wccnet.org/admin/security/service.html

## Slide 4: Eric S. Raymond Author and Open Source Guru
What is Open Source and how it will affect you
Author of “The Cathedral and the Bazaar”, the paper that convinced Netscape to release its source code to the public
Wed., Jan. 19th at 7:30PM in Morris Laurence Bldg., WCC campus
Sponsored by Washtenaw Linux Users Group
http://www.lugwash.org/meeting.html

## Slide 5: Win2000 pricing announced
Windows 2000 is $319 (same as NT 4.0 Workstation
Upgrade price from Windows NT is $149 or $219 from Windows 95 or 98.
The five-user upgrade version of Windows 2000 Server will cost $499 or $999 for the full retail version.
A 10-user version will go for $1199 or $599 as an upgrade from Windows NT or Novell NetWare.

## Slide 6: Revisit CNT 211 Website http://www.HAL9K.com/cnt211

## Slide 7: Review Lecture #1

## Slide 8: CH.3 Your Job as Administrator
Installing Servers
Managing Servers
Managing the Network
Maintaining Network Security
Protecting Data
Documenting the Network
Supporting and Training Users

## Slide 9: Installing Servers
What makes a “server”?
  Large amounts of RAM (256MB - 1024MB)
  Large hard disks
  SMP support
  Fault Tolerance
Improving Fault Tolerance
  Uninterruptable Power Supplies (UPS)
  RAID
  Error Correcting Memory (ECM)
  Network alerts

## Slide 10: Managing the Server
Know the normal values of performance statistics
Consult the current statistics when problems arise
Statistics justify capacity planning before disaster sets in

## Slide 11: Installing the Network
Professional installation needed for large offices ( >10 stations)
Manufactured cables may be more reliable than hand-rolled
Understand the cabling of the existing network before making changes

## Slide 12: Maintaining Security
Firewalls (not covered in this class)
Tradeoff: more security, less “friendly”
Establish written and understandable policies
Get management buy-in

## Slide 13: Protecting Data
Backup must occur nightly
Have a written plan, make sure its executed
Backup is not sexy, until disaster strikes
  hardware failure
  user failure
  security failure
  virus

## Slide 14: Documenting the Network
Don’t rely on your memory
Good documentation makes increasing staff easier and vacations possible
Every cable should be identified on both ends
Hub-level wiring diagram should be kept current
Your manager requires:
  accurate inventory including serial numbers
  records for maintenance contracts and leases

## Slide 15: Supporting Network Applications
Installing software over the network
You are the help desk
Determine user workstation needs
Training users
Intranet help pages (local FAQs)

## Slide 16: CH.4 Planning and Installing Network Media
Common Characteristics of Media
Electromagnetic Interference (EMI)
Bandwidth
Costs
Media Types
  Coax
  STP
  UTP
  Fiber

## Slide 17: Errors
“100Mbit is about the limit of bandwidth for UTP Cat5” (p. 52)
  1000BaseT will use Cat5
“Some Ethernet NICs are less than $100” (p. 75)
  $20 is the street price for Ethernet NICs

## Slide 18: Common Characteristics of Media
1. Electromagnetic Interference (EMI) Sensitivity
2. Bandwidth
3. Cost
No single media fits all problems!

## Slide 19: Electromagnetic Interference (EMI) Sensitivity
Any dynamic magnetic field causes static in copper LAN cables
  e.g. Florescent lights, electric motors, lightning
LAN cables produce a magnetic field (radio)
Thus a risk exists of clandestine reception
  An all-fiber optic network can be substituted
  Or use of completely encrypted data

## Slide 20: Bandwidth
Everyone talks about it, nobody does anything about it
UTP Cat 4: 20Mbit/sec in full duplex mode
UTP Cat 5: 100Mbit sec in half duplex mode
Demanding applications for bandwidth
  videoconferencing
  server-to-server communications (e.g. clusters)
  backup over the network

## Slide 21: Types of Bandwidth
Baseband: entire bandwidth is devoted to one data signal (UTP)
Broadband: bandwidth carries multiple signals simultaneously, receiver “tunes” in (cable TV)

## Slide 22: Costs
Cable
  pre-made cost 3 to 10 times as much as hand rolled
NICs
  from $20 to $200 (server rated)
Hubs
  active (cheap)
  switched (medium)
  managed (higher)

## Slide 23: Types of Media
Coaxial
Shielded Twisted Pair (STP)
Unshielded Twisted Pair (UTP)
Fiber-optic

## Slide 24: Coaxial cable
RG-11, RG-8: obsolete “thick” coax
RG-58: thinnet, BNC, 10Base2 (see picture)
RG-59: TV cable, broadband only

## Slide 25: RG-58 “thinnet”
Advantages
  Shielded for EMI resistance
  Reliable if not altered
Disadvantages
  Bus topology is difficult to add/remove stations
  Hand-rolled cables can be balky
  Useless at speeds above 10Mbit

## Slide 26: Shielded Twisted Pair (STP)
Two insulated wires twisted together
Used for token ring
Advantages
  Built-in EMI cancellation
  Sturdy and durable
Disadvantages
  Not 100% EMI-proof
  Bulky
  Top speed usually 16Mbit

## Slide 27: Unshielded Twisted Pair (UTP)
Two pairs, no shield, RJ-45 connector
Many grades of cable available
Should be wired professionally
UTP Cat5 recommended for all new installs

## Slide 28: UTP “Categories”
Cat 1: Voice-grade
Cat 3: 10Mbit Ethernet or 16Mbit Token Ring
Cat 4: 20Mbit (full duplex) Ethernet
Cat 5: 100Mbit+ bandwidth
Cat 7: 2.4GBit for ATM equipment

## Slide 29: UTP: Pros and Cons
Advantages
  Most inexpensive cabling
  Lightweight and compact
  Installation straightforward
Disadvantages
  High EMI potential (see Cat 5e)
  Gigabit standards not fully accepted

## Slide 30: Fiber-Optics

## Slide 31: Fiber-Optics
Fast: 1GBit+ rates
Far: 100s of miles
EMI: None!
Cost: most expensive but can be justified
  Server-to-server communications
  Long haul campus interconnect
  WANs in general
  Sound long-term investment

## Slide 32: Cost of Fiber-Optics
Cable cost similar to Cat5 in bulk
Fiber NIC cards about $250
  Compare to $20 for Cat5 NIC
12-port hub $1500
  Compare to $100 for Cat5 hubs

## Slide 33: Copper vs. Fiber
Fiber takes less space in the conduit
Fiber is immune to EMI and eavesdropping
Fiber is corrosion proof and reliable
Fiber bandwidth considered unlimited
  “Fiber is forever”

## Slide 34: Summary of Cable Characteristics

## Slide 35: Wireless Media
Optical Link: infrared or laser
RF (“Radio”) Link: microwave, UHF
Most often used when public right-of-way prevents cabling

## Slide 36: Optical Link
Similar to IR ports used on laptops
Large room optical link uses infrared
Point-to-point laser link between buildings
Bandwidth low considering the cost (<5Mbit)

## Slide 37: RF LAN
Spread Spectrum
  Uses multiple frequencies simultaneously
  Unlicensed frequencies “free for all”
  Can work through walls
18Ghz Cellular
  Motorola proprietary, licensed nationwide
  Hybrid of wires/wireless

## Slide 38: Topologies
All topologies based on bus or point-to-point
Bus: all devices hear the signal
Point-to-Point: two devices on the end of a wire
What kind of topology are the following?
  Parallel port
  Mouse port
  PCI, ISA

## Slide 39: Bus Network
Machine 1
Machine 2
Machine 3
Devices connect to the bus in “T” junctions
Always terminated on both ends
Most often used with “thinnet”
One bus segment shown below:
termination

## Slide 40: Point-to-Point Links
Half-duplex: one device talks then “turns over” the channel
Full-duplex: both devices can send messages in either direction simultaneously (see pic)
  In two-pair wiring, this is done by dedicating one pair to transmit each way
Machine 1
Machine 2
T
R
T
R

## Slide 41: Building Networks with busses
Bridge connects multiple bus segments
A bridge may include a switch to filter packets
Machine 1
Machine 2
Machine 3
Machine 4
Machine 5
Machine 6
Bridge

## Slide 42: (Token) Ring Networks
Each device can receive from one neighbor and transmit to one neighbor
Machine 1
Machine 2
Machine 3
Machine 4
T
R
T
T
T
R
R
R

## Slide 43: Star Network
All machines connect to a hub
Machine 1
Machine 2
Machine 3
Machine 4
Hub

## Slide 44: Advantages of Star Topology
Easy to expand without disrupting service
Bad devices can be isolated
Managed hubs allow remote control
Only way to go for UTP Cat5

## Slide 45: Physical vs. logical topologies
You cannot rely on just cabling to guess the topology
A network wired as a star could be functioning as a ring (p. 62)
A network wired as a star could be functioning as a bus (p. 63)
Difference is due to the switch wiring inside the hub

## Slide 46: More about hubs
Passive: unpowered, useful only for token ring
Active: powered and may have some signal processing functions (see list)
  Amplification
  Reshaping/retiming of distorted signals
  Problem detection
  Send performance and error reports
  Switching hubs increase total bandwidth
  Managed hubs allow remote control

## Slide 47: Switching Hubs (p. 73)
Switching: allows private point-to-point connections between two peers
Each point-to-point connection enjoys 100% of the bandwidth, not just a share of it.
Machine 1
Machine 2
Machine 3
Machine 4
Switching Hub
100%
100%
200% utilization!

## Slide 48: Managed Hubs
Technologies for controlling Managed Hubs
  SNMP: Simple Network Management Protocol
  Web-based interfaces including java
  Login via Telnet client
Management features
  Enable/disable one port at a time
  Gather/report statistics in real time
  WAN control and routing features
  RMON: Remote MONitoring protocol

## Slide 49: Intel’s Device View for Managed Hubs

## Slide 50: Hub Technologies Comparison

## Slide 51: LAN Cabling Standards
IEEE: International Electrical and Electronics Engineers
IEEE LAN Standards Committee (“802”)
  802.2 Logical Link Control (LLC) layer
  802.3 IEEE Ethernet
  802.3z 1000BaseT
  802.5 IEEE Token Ring
ISO: International Standards Organization
  ISO 9314: Fiber Distributed Data Interface (FDDI)

## Slide 52: Ethernet
Dates back to 1970s at Xerox
Standardized as IEEE 802.3
Originally used with coax (RG-11, RG-8, RG-58) but now embraces all media
Based on bus topology
Key technology is CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  “Listen Before Talking”

## Slide 53: Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Carrier Sense: listens to see if network is busy
  if it is busy, then it will wait a while and try again
Multiple Access: implies simultaneous listening
Collision Detection: stop talking if someone else starts talking
  Rise in line voltage indicates “collision”
After a collision, wait a random time period before re-transmission
  Randomness avoids deadlock

## Slide 54: Why does CSMA/CD work?
Frames are small: 1,518 bytes (~12Kbits)
Bandwidth is large: 10Mbits +
Traffic load can never reach 100%
  Can accept constant loads up to 30% capacity
  Can accept traffic bursts up to 60% capacity
Probabilistic access control method means there is no guarantee when you can get thru
Token ring provides predictable delivery rates

## Slide 55: Ethernet Cabling
Thick Ethernet (10Base5): no longer used
Thin Ethernet (10Base2): coax with BNC
Twisted-Pair Ethernet (10BaseT): star wiring topology which requires hubs and UTP cables
  The 10 means 10Mbit,
Newer variants are 100BaseT (100Mbit) and 1000BaseT (1000Mbit or 1GBit)

## Slide 56: 10Base2 / 10Base5 limits
Bus topologies always have a max number of devices that can be supported
Repeaters can be used to double maximum length limits
Bridges must be used to link segments
  If a segment grows too long, it must be split
  If a segment has too many devices, it must be split
BNC T-connectors mean cables must be cut to insert a new device

## Slide 57: Comparison of 10Base5 and 10Base2 (p. 70)

## Slide 58: Twisted-Pair (10BaseT)
Unshielded Twisted Pair (UTP), Cat5 preferred
Requires star topology based on hubs
Superior reconfiguration and management
Two types of cabling required (p. 71)
  Straight-thru: connects device to hub
  Crossover (“X”): connects hub-to-hub or point-to-point (2-station network)

## Slide 59: 100BaseT
100BaseTX: uses UTP Cat5
Collision Domain: longest network you can build without switches, bridges, or routers
  10BaseT can run 2500m (1.5miles)
  100BaseT can run 250m (820 feet)
You will probably use dual-speed (10/100) switches to allow 10BaseT and 100BaseT to coexist

## Slide 60: 100VG-AnyLAN
HP and IEEE 802.12 standard
Not an Ethernet in the signalling sense
Uses Demand Based Priority Access to moderate collisions
Exceeds size limits of 100BaseT
Supports Ethernet and token ring frames
Not in very widespread use

## Slide 61: Token Ring
IBM and IEEE 802.5 standard
Why nobody likes Token Ring
  NICs and hubs cost 8x as much as Ethernet
  Can’t escape its proprietary past
  Managing token ring requires software tools
  16-Mbit speed limit
Why you might have to use it
  Deterministic access control is suitable for real-time (e.g. factory floor) operations
  IBM Legacy sites

## Slide 62: Token-based Access Control
Token: a special type of data frame that circulates around the logical ring
Machine 1
Machine 2
Machine 3
Machine 4
T
R
T
T
T
R
R
R
Token

## Slide 63: Token Access Control Rules
A device can transmit only when its in possession of the token
It must wait until the token arrives
After the device transmits data, its token is released to the network
There is a maximum transmission unit (MTU) to prevent over-utilization.

## Slide 64: The Ring Error Monitor (REM)
REM is your referee since all stations are equal
Handles lost tokens and initial token
Tells what to do if data stops flowing
Identifies frames bound for systems which are off-the-network or down

## Slide 65: IBM Cabling system
IEEE 802.5 does not specify cabling
IBM jacks allow ring to remain unbroken when unplugged (p. 77-8)
Most token rings use a physical star topology and the hub implements the logical ring
8228 MSAU (Multi Station Access Unit) is a passive hub
CAU (Controlled Access Unit) is active hub

## Slide 66: Token ring limits
Up to 260 devices and 33 MSAUs in a ring
Segment can be up to 100m
Repeaters can extend the length
Supports STP (Type 1 and 2) and UTP
4Mbit and 16Mbit are only speeds available

## Slide 67: Fiber Distributed Data Interface (FDDI)
FDDI drivers included with Windows NT
FDDI is 100Mbit that functions like token ring
FDDI networks often use two rings to route frames in opposite directions (dual-attached)
Most often used as backbone because the rings can run up to 100km (60 miles)
Doesn’t handle workstations being turned on and off very well
See illustration p.80

## Slide 68: Structured Cabling Systems
When more than 3 dozen PCs are involved, cabling becomes a nightmare spaghetti
Structured cabling pulls all wires into centralized wiring closets (one per floor)
Jack panels are installed in all cubicles
Wiring ends at a patch panel and then is fed into rack-mounted hubs (24 or more ports)
Always professionally installed and use miles of cable

## Slide 69: Concentrators and Stackable Hubs
Concentrators: allow several types of media to be integrated in the wiring closet
  Expandable by adding media-specific plug-in cards
Stackable Hubs: designed to work together
  cascade port connects like hubs together
  management information can be accumulated or shared

## Slide 70: Planning Network Cabling
How many computers now? Next year?
Overall bandwidth requirements
Physical barriers
Open drop areas for transient users
Locations of hubs or terminators
Bridges to connect bus segments
Policies and procedures

## Slide 71: Installing Network Cabling
Best time is when building is under construction or before move-in date
Consider buying a cable tester and cable making tools
Raceways can be used where ceilings are not open to cables
Don’t try to do fiber installation yourself

## Slide 72: CH. 4 Review questions
What methods can be used to improve fault tolerance on a server?
What situations might require you to restore a backup?
What type of network is STP media used for?
What is the difference between baseband and broadband?
What type of media would you choose if EMI suceptibility is the primary concern?

## Slide 73: CH. 4 Review (cont.)
What media might you use to link two offices in adjacent skyscrapers?
What makes bus topology different than point-to-point?
How can two busses talk to each other?
When would you choose 100VG-AnyLAN over 100BaseT?
Two reasons why not to choose Token Ring?
What is a backbone and what type of media is appropriate for it?

## Slide 74: Lab shakedown exercise
Format up Ghost diskettes for everyone
Restore default NT Server setups from the network
Verify that the NT Server is restored OK
Save the student's work up to the network.

## Slide 75: Quick tour of NT Administration tools
Task Manager
Windows NT “Diagnostics”