## Slide 1: CNT211
Lecture 3
1/27

## Slide 2: Agenda
What’s on the class website?
Review questions from lecture #2
Student questions from lecture #2
CH.5 Selecting Hardware for Windows NT
Distribute Assignment #1
Lab Assignment #0

## Slide 3: http://www.HAL9K.com/cnt211
CNT 211 Syllabus (PDF)
Buy the textbook online bookstore
How to get on/off the CNT 211 mailing list
Find out about weather-related school closings
Class assignments (download)
Lab info sheet (PDF)
Microsoft Great Lakes Win2000 events
URLs from Lectures

## Slide 4: Review Questions from lecture #2

## Slide 5: Student questions from lecture #2
1000BaseT and Cat5
Broadband: analog or digital?
What are link segments?
5-4-3 rule

## Slide 6: 1000BaseT and Cat5
1000BaseT adapters retail about $600
1000BaseT originally assumed fiber optics only
“The 802.3ab specification should work fine with existing Category 5, as long as it’s been tested and certified.”
Cat5e works even better with 1000BaseT too
TIA standards for Cat6 and Cat7 pending
http://www.networkmagazine.com/magazine/archive/1999/08/9908cov.htm
http://www.gigabit-ethernet.org/

## Slide 7: Broadband: analog or digital?
Broadband is an analog carrier divided into different ranges which could be called bands or channels
A particular band might have digital or analog modulation
“Its all analog at the electrical level” (i.e. voltage)
RG-59 coax and fiber are broadband
STP and UTP are baseband

## Slide 8: What are link segments? (p. 68)
Ethernet segment is the coaxial cable between two terminators
Link segments are used in coaxial baseband cabling (thicknet or thinnet)
Link segments have no devices attached to them except repeaters
When the segment length limit (500M or 185M) is reached, a repeater can be used.

## Slide 9: “5-4-3 Rule”: Applies to Collision Domains
Collision Domain: the scope of a network that can be built without bridges, switches, or routers
Between any two nodes on the network there can only be a maximum of 5 segments, connected through 4 repeaters/concentrators. In addition, only 3 of the segments may be populated (trunk) segments if they are made of coaxial cable

## Slide 10: CH.5 Selecting Hardware for Windows NT
RISC CPUs
Intel family
Busses (ISA, PCI, and AGP)
Memory
Hard Drives (IDE and SCSI)
Server hardware configuration

## Slide 11: Errors and notable omissions
Failure of non-Intel NT systems (p. 92)
Pentium III and later CPUs omitted (p. 99)
Should read “symmetrical processing” (p. 99)
  not “asymmetrical”
Minimum configuration is ridiculous (p. 100)
AGP bus omitted (p. 103)
RDRAM (p. 107)
Missing some new SCSI variants (p. 113)
Table 5-3: “bandwidth” should be “bus size”

## Slide 12: RISC vs. CISC
RISC = Reduced Instruction Set Computer
  Fewer and shorter machine instructions to get the job done
  Examples: PowerPC, MIPS, Alpha
CISC = Complex Instruction Set Computer
  Long and complex multi-byte instructions (VLIW)
  Examples: 386, 486, Pentium I/II/III

## Slide 13: What is an Instruction Set?
Instruction Set: binary operation codes (“op codes”) for arithmetic, logic, and branching
Binary Compatible: If two CPUs can run some programs written in the same instruction set
Binary Compatibles: AMD K7 and Pentium III
Binary Incompatible:
  Pentium and Motorola MC68040
  SUN Sparc and Cray Y-MP supercomputer
  Z-80 and 6502
  More often the rule than the exception

## Slide 14: What are RISC CPUs?
PowerPC: a “super-chip” created by Apple, IBM, and Motorola, in 1991
  One chip capable of running three OSes! MacOS, AIX (IBM Unix), and Windows NT
Alpha AXP: Created by DEC, now owned by Compaq
  Can run Ultrix/OSF (Unix), Windows NT, maybe Windows 2000 (?)
MIPS R4000: Created by MIPS Inc., used by Silicon Graphics (SGI) Inc
  Can run IRIX (Unix) on SGI, Windows NT

## Slide 15: Why didn’t RISC take over the world?
Required 64MB RAM when RAM was $40/MB
  64 x 40 = $2560 bigger price tag
IBM tried to delay PowerPC shipments until OS/2 for PowerPC was ready (never shipped)
Apple had no interest in making non-Mac OS software work
RISC represented high prestige but tiny revenue to Microsoft

## Slide 16: RISC CPUs for Windows NT
Originally held out greatest performance hopes
Market realities quickly set in
  Microsoft would not release apps compiled for RISC
  Poor software development tools
  Software emulation of Intel CPUs was “good enough”, although only 25% as fast as native code
“Compared with Pentium PCs, they don't offer advantages in performance or price, and native software remains rare.” PC Magazine (10/95)

## Slide 17: The death march of RISC for NT
PowerPC for NT considered DOA 1995
  “IBM and Motorola announced in December 1996 that they will no longer sell systems with Windows NT. The current release of NT will be supported, but Microsoft will not release any future versions for the PowerPC.”
MIPS chip unsupported 1997
DEC Alpha chip unsupported 1999 (August)
“Support for non-Intel Novell clients is not available” (Windows Magazine, 3/98)

## Slide 18: Intel Pentium family
Pentium Pro
  First CPU easy to use for up to 4-way SMP designs
Pentium II (“Deschutes”)
  Slot 1: for desktop computers
  Slot 2: (“Xeon”) for servers
Pentium III (“Katmai” or MMX2)
  70 new multimedia instructions (SIMD)
  “Xeon” variant also available for servers
http://developer.intel.com/design/processor/

## Slide 19: The IA-64 future?
IA-64: Intel Architecture for 64-bit CPUs
NT support for Merced announced in 1996
Merced renamed to Itanium in October 1999
“Itanium processor-based servers and workstations will be available in the second half of the year 2000.” Intel press release

## Slide 20: Intel CPU speeds
Intel Celeron and AMD K6 not recommended for servers

## Slide 21: Volkman’s Minimum NT Workstation configuration guide
Pentium 400Mhz+
PCI bus (100Mhz is better)
8GB hard disk
64MB RAM (128MB if you plan on Win 2000)
2MB Video RAM

## Slide 22: Microcomputer busses
The bus provides a group of expansion slots
Expansion slots help stave off obsolescence
  Network Interface Cards (NICs)
  Video graphics accelerators (VGA)
Once a feature is standardized it is moved down to the motherboard
  Serial ports, parallel ports, mouse ports
  Disk controllers, audio support
A motherboard may have several busses

## Slide 23: Busses become obsolete over time
ISA 8-bit: 1982 - 1984
ISA 16-bit: 1984 - Present
Microchannel (IBM): 1987 - 1992
EISA: 1988 - 1992
VESA Local Bus: 1993 - 1994
PCI Bus: 1996 - Present
AGP Bus: 1997 - Present

## Slide 24: ISA 16-bit bus
Introduced by IBM for PC-AT in 1984
Simple to develop low-cost and reliable hardware adapters for it
Inappropriate for advanced applications:
  Fast SCSI 3
  100Mbit NICs
Still common in current motherboard designs due to its pervasiveness
Manual configuration of resources (usually)

## Slide 25: PCI bus
Peripheral Component Interconnect (PCI)
True 64-bit bus design
Clock rates of 66, 100, and 133Mhz
Limited to 3 slots without PCI Bridge
Works well in conjunction with AGP Bus
Plug-and-play design (Win 9x and Win 2000)
Power management features (PCI 2.1)
http://www.pcisig.com/

## Slide 26: AGP (Advanced Graphics Port) Bus
High speed interconnect solely for graphics
Graphics are the most demanding peripherals
Scalable bus speed: 1x, 2x, 4x
Moves 1GB/sec at 4x
Does not impact PCI or memory bus bandwidth
Now found in laptops too
AGP 2.0 released in May 1998
http://developer.intel.com/technology/agp/

## Slide 27: Characteristics of Expansion Buses

## Slide 28: ISA, PCI, and AGP Together:

## Slide 29: Types of Memory
ROM: Read-Only Memory (e.g. BIOS)
RAM: Random Access Memory
  includes DRAM, EDO DRAM, SDRAM, RDRAM, …
SRAM: Static RAM
  used as cache or adapters like NICs

## Slide 30: Access Time and Wait States
Access time measured in nanoseconds (ns)
  1 second = 1 billion nanoseconds
  1 nanosecond = 17 inches
If memory is not ready when the CPU needs it, a wait-state occurs (like a timeout)
Rule-of-thumb to achieve zero wait states:
  “buss speed in Mhz times access in ns = 1000”
For 100Mhz bus:
  10 ns = 0 waits, 20 ns = 1 wait, 30 ns = 3 waits

## Slide 31: Main Memory RAM Types
EDO DRAM: Extended Data Output (EDO)
  Runs at slow PCI bus speeds up to 66Mhz
SDRAM: Synchronous Dynamic RAM
  Runs at PCI bus speed: 100Mhz = 10ns 133Mhz = 6ns
RDRAM: Rambus Dynamic RAM
  Runs at PCI bus speed: 200Mhz = 5ns 600Mhz = < 2ns
  Predominant by end of 2000

## Slide 32: Preventing Memory Failures
Overheating is the most common reason
Parity checking: additional bit per byte
  Knows when it fails, but not how to fix itself
ECC: Error Correction Code
  Knows when it fails and how to fix it
  Much more expensive

## Slide 33: Windows and RAM

## Slide 34: Hard Drives
IDE/EIDE: Integrated Drive Electronics
  Disk controller inside the drive
SCSI: Small Systems Computer Interface
  Disk controller external to the drive Usually a plug-in adapter
SCSI Fibre Channel
  Harnesses a fiber optic network

## Slide 35: IDE/EIDE channel
IDE (ATA): 2 hard disks (one channel)
EIDE (ATA-2): 4 devices (two channels)
EIDE supports CD-ROM, CD-RW, ZIP disks, and tape drives via ATAPI protocol
EIDE predominant since 1997
Master/slave controller arrangement
Cheapest technology for hosting disk drives

## Slide 37: IDE Master/Slave
Each IDE channel must have a single master
Master: the drive whose controller is active
Slave: the drive whose controller is disabled
Roles are determined by jumpers or special cable (less common)
Bootable hard drive must be master on channel “0”

## Slide 38: Typical IDE jumper block

## Slide 39: IDE Resources
Even though its not on a bus, IDE still requires system resources
IDE channel 0 uses IRQ 14
IDE channel 1 uses IRQ 15

## Slide 40: IDE and Servers
Four disk maximum may not be enough
Only one drive on each channel can be busy
IDE not well suited to disk mirroring
  Slave controller cannot take over if master dies
  If mirrored drive is on the same channel, everything takes twice as long
EIDE drives not as big as SCSI (2 - 4x)

## Slide 41: Ultra DMA/33 (“Ultra ATA”)
Direct Memory Access (DMA) allows a peripheral transfer data to the system’s memory without control from the CPU
DMA increases speed by using the DMA controller to manager the data transfer rather than the processor. The operating system must have a DMA capable driver installed before DMA can be used.

## Slide 42: Bus Mastering and DMA
Bus Mastering DMA allows the interface card, or drive controller, to manage the transfer of data from the drive directly to the system’s memory.
Ultra DMA (UDMA) is the latest ATA bus mastering DMA protocol. It doubles the maximum data transfer to 33.3 Mbytes/sec.
http://www.seagate.com/support/kb/disc/ultra_ata_faq.html

## Slide 43: Small Computer Systems Interface
SCSI standard maintained by ANSI
Supported on Unix, Macintosh, PC, etc.
Deals in blocks of data, not track/sector/head
Supports disks, CD-ROM, CD-RW, tape drives, scanners, and ...
Can be used for jukebox implementations
  Example: CD-ROM jukebox with 100 CD-ROM cartridges and 4 drives
Supports many devices (7 to 15) on a bus

## Slide 44: SCSI standards
SCSI-1: 5MB/sec, 7 devices, 8-bit bus
SCSI-2: includes parity checking and bus disconnnect.
SCSI-2 legal variants:
  SCSI Fast: 10MB/sec
  SCSI Wide: 16-bit bus (“wide”)
  SCSI Fast-Wide: both of above
SCSI-3: a family of solutions, not a single spec

## Slide 45: More SCSI standards (ugh!)
SCSI-3 Fast-20 (“Ultra SCSI”): supports narrow (20MB/s) and wide (40MB/s) busses
SCSI-3 Fast-40 (“Ultra2 SCSI”): supports narrow (40MB/s) and wide (80MB/s) busses
LVD: Low Voltage Differential allows longer cable lengths and faster bus speed
Fast-80: supports wide (160MB/s) bus
http://www.seagate.com:80/support/kb/disc/scsirev.html

## Slide 46: SCSI Fibre Channel
Fibre channel is a Serial interface
Can be used with coax or fibre optic
Transfer rate 100MB/sec
Up to 126 devices

## Slide 47: Know your SCSI
SCSI Narrow
SCSI Wide
SCSI SCA-2
hot-pluggable

## Slide 48: SCSI Standards Comparison

## Slide 50: Disks for servers
Multiple SCSI drives always outperform IDE
SCSI always costs more than IDE
SCSI configuration can be confusing
SCSI bus disconnect allows more devices to be active simultaneously
SCSI hot-pluggable drives help fault tolerance
Recommended: SCSI-2 Fast-Wide unless budget mandates IDE

## Slide 51: Assignment #1
Short answers which justify your choice of technologies
Requires some research using the web
Goal: to integrate your thinking about various small pieces of technology

## Slide 52: Assignment #0:
Drill on saving and restoring NT configurations from the Novell Network server
Goal: proficiency will allow you concentrate on solving assignments #2-5.

## Slide 53: Review Questions
What three busses are still in common use today?
What does “5” stand for in the 5-4-3 rule?
Why would you avoid using ISA bus cards?
Which type of main memory RAM is fastest?
Why would you avoid use EIDE for servers?
Why is SCSI a good choice for servers?